## Slide 1: Quantifying the Promise of Lithium-Air Batteries for Electric Vehicles
Kevin Gallagher1, Steve Goebel2†, Tom Greszler2‡, Mark Mathias2,
Wolfgang Oelerich3§, Damla Eroglu1, and Venkat Srinivasan4
1Argonne National Lab, 2General Motors, 3Opel AG, 4Lawrence Berkeley National Lab
†currently: SimuTech Group; ‡currently: Saft America; §Wholly owned subsidiary of GM
Carnegie Mellon University Nov 25 2013

## Slide 2
Transportation 29%
Residential & Commercial
Non-electric
11%
Electricity
Residential
15%
Electricity
Commercial
15%
Electricity
Industrial
10%
Industrial
Non-electric
20%
EIA Annual Energy Review 2009
Two biggest energy uses poised
for transformational change
Transportation 29%
  Oil  Electricity
  Reduce foreign oil dependence
  Reduce carbon emissions
Electricity 40%
  Coal  Gas  Wind and Solar
  Reduce carbon emissions
  Sustainable energy supply
Energy Demand
The bottleneck for both transitions is
inexpensive, high performance electrical energy storage
Energy Storage Opportunity

## Slide 3: JCESR: DOE’s Battery and Energy Storage Hub
Multivalent Intercalation
Chemical Transformation
Non-Aqueous Redox Flow
CROSSCUTING SCIENCE
Systems
Analysis and Translation
Cell Design and Prototyping
Commercial Deployment
DOE Basic Energy Sciences (BES) with a twist
    Traditional science approach – let one thousand flowers bloom
    JCESR approach to accelerate innovation
      Integrating science through prototyping/industry (R and the DDD) on day 1
      Generating the necessary understanding to control atomic and molecular process to produce prototypes that meet our challenging goals
      Reconfiguring work in response to new insights
      Communication, communication, communication

## Slide 4
The JCESR Partner Team
National Laboratories
Argonne
Lawrence Berkeley
Sandia
SLAC
Pacific Northwest
Discovery Science
Battery Design
Research Prototypes
Manufacturing Collaboration
Universities
University of Illinois at Chicago
University of Illinois at Urbana-Champaign
Northwestern University
University of Chicago
University of Michigan
Faculty from
MIT, University of Waterloo,
Harvard, Notre Dame
Private Sector
Johnson Controls (JCI)
Dow
Applied Materials
Clean Energy Trust
Individuals from
General Motors
United Technologies Research Center
Multivalent Intercalation
Chemical Transformation
Non-Aqueous Redox Flow
CROSSCUTING SCIENCE
Systems Analysis and Translation
Cell Design and Prototyping
Commercial Deployment

## Slide 5
JCESR’s Beyond Lithium-ion Concepts
Multivalent Intercalation
Chemical Transformation
Replace monovalent Li+ with
di- or tri-valent ions: Mg++, Al+++, . . .
Double or triple capacity stored and released
Replace intercalation with high energy chemical reaction:
Li-S, Li-O, Na-S, . . .
Replace solid electrodes with liquid solutions or suspensions:
lower cost, higher capacity, greater flexibility
Non-aqueous Redox Flow
Tailored structure-function relationships
Redox couples, electrolytes, SEI . . .
Cross-cutting opportunity
Designer Organic Molecules
Black, Adams, Nazar, Adv. Energy Mater 2, 801 (2012)
Yang, Zheng, Cui, Ener Env Sci 5, 1551 (2013)
electrons
ions
Notes: Lets go back to the roadmap diagram.

## Slide 6: JCESR: Focused on Beyond Li-ion Technologies
Multivalent Intercalation
Chemical Transformation
Non-Aqueous Redox Flow
CROSSCUTING SCIENCE
Systems
Analysis and Translation
Cell Design and Prototyping
Commercial Deployment
Anodes: metals Li, Mg, Ca, etc
Cathodes: S, O2, etc
Mg2+, Ca2+, Zn2+, Al3+ Intercalation cathodes
Electrolyte development
Solutions approach (redox active molecules)
Suspensions approach (flowable electrodes)
In a world of limited research $$$, where should focus be placed?

## Slide 7: Vision for Systems Analysis and Translation
Transformation functions that tie system level goals to materials level values
    What cell voltage, capacity, diffusion coefficient, etc., do I need to meet Hub goals?
  Directing research dollars to most promising approaches
    Informing JCESR leadership, assessing most promising candidates, creating new TDTs
  Understanding the barriers to reaching transformational advances
    Across all levels – materials, electrodes, cells, pack/stacks
5-5-5
Building a battery on the computer

## Slide 8: Specific energy and energy density
Amount of energy within a mass/space
Increasing energy density (Wh/L) decreases cost ($/kWh)
  Belief (meaning not always true)
Theoretical values and achieved values are very different
A calibration: Uranium-235 >>> Liquid Fuels > Battery Materials

## Slide 9: The lithium-air (oxygen) battery: Motivation
A high-visibility archetype of the “best-case” battery
Oxygen is light and has a high standard potential
Oxygen can be an unlimited resource – air is all around us
Only carry the oxygen you have reacted – gains mass over time
Nonaqueous has received greatest attention to date
  Higher theoretical specific energy (Wh/kg) values
  Does not require the reversible aqueous oxygen electrode
  Product has been shown to be lithium peroxide (ignoring side rxns)
2Li+ + 2e- + O2 ↔ Li2O2 Uo = 2.96 V vs Li

## Slide 10
Li/Li2O2 ≈ 3,458 Wh/kg
3,445 Wh/L
Li-ion ≈ 400 Wh/kg
1,400 Wh/L

## Slide 11: Framework for this optimistic / best case study
Assume proposed solutions to problems will work (no life issues)
  Solved all the chemistry problems
  Engineering solutions to overcome known issues
Evaluate a range of performance values
  Up to electrode thickness limitations (200 microns)
  Assume mass transfer limits have been engineered away
Examining a 330 mile battery with modest power (100 kWhuse, 80 kWnet)
  Minimizing fixed system contributions (compressor, separations)
  Low P/E ratio results in thicker electrodes
Favorable systems-level assumptions
  Best case H2O/CO2 separations values
  No penalties for ducting or access to system components (typically 2x)
High manufacturing volumes, competitive market
Goal is to project how good can it be (hard), rather than what is the most likely outcome (impossible)

## Slide 12: Process flow of design & cost battery model
Bottom-up performance and cost model
  Account for each component necessary to make functioning battery
  Captures manufacturing cost by building the facility for each battery
Builds upon BatPaC: Peer-reviewed Li-ion model www.cse.anl.gov/batpac
Notes: BatPaC is a freely available Li-ion Battery Performance and Cost model supported by DOE EERE-OVT and developed at Argonne National Laboratory. The model and supporting documentation are available from www.cse.anl.gov/batpac . BatPaC has been subjected to multiple public and private peer reviews that culminated in its use by the EPA in the 2017-2025 light duty vehicle GHG and CAFE rule.
This Li-O2 model uses BatPaC as a framework but substantially revises the performance calculation and adds new modeling capabilities to size and analyze the requirements of delivering, purifying, and/or enclosing a gaseous reactant.

## Slide 13: Materials in a single layer of Li/O2 cell
50% excess
Negative electrode
  Lithium-metal, 50% excess
  Solid ceramic electrolyte
  Hermetic, long-lived seal
Positive electrode
  Carbon-like porous felt
  Liquid electrolyte
  60 vol% Li2O2 at discharge
Flow-field/positive current collector
  0.3 MPaa Air: corrugated Al foil
    Sized for 30 kPa pressure drop
    Optimistically assume 20 um thickness
  Pure O2: standard battery Al foil
    Porosity of electrode is enough

## Slide 14: Multiple scales and approaches to design
Electrode Sizing
Pack & System
Closed system
Open system
Li-O2 Chemistry
Cell & Module
50% excess Lithium

## Slide 15: Closed vs Open Architecture for Li/O2
Li2O2 product reacts irreversibly with CO2
Water must also be removed
Target impurity levels near 1-10 ppmv
Notes: BatPaC is a freely available Li-ion Battery Performance and Cost model supported by DOE EERE-OVT and developed at Argonne National Laboratory. The model and supporting documentation are available from www.cse.anl.gov/batpac . BatPaC has been subjected to multiple public and private peer reviews that culminated in its use by the EPA in the 2017-2025 light duty vehicle GHG and CAFE rule.
This Li-O2 model uses BatPaC as a framework but substantially revises the performance calculation and adds new modeling capabilities to size and analyze the requirements of delivering, purifying, and/or enclosing a gaseous reactant.

## Slide 16: Compare Li/O2 estimates in context of Li-ion
Traditional Li-ion will continue to improve
  Use graphite vs LiNi1/3Mn1/3Co1/3O2 as baseline (Gr/NMC333)
Advanced Li-ion will build upon Li-ion improvements
Consider a silicon-alloy composite anode
  1300 mAh/g @ 0.32 V vs Li, 50 vol% electrolyte in discharged state
  Prelithiated to overcome 1st cycle losses
Consider Lithium- and Manganese-Rich NMC cathode (LMRNMC)
  225 mAh/g @ 3.75 V vs Li
  Assumes no voltage fade and impedance similar to NMC333
Pair advanced Li-ion with a Li-metal anode

## Slide 17: Systems level energy density and specific energy
What’s in the bubbles?
Range of performances (electrode thickness)
Range of cell parallel/series configurations
This does not include other, more pessimistic outcomes for the Li/O2 systems level projection
Side notes
Diminishing returns at higher Wh/kg, Wh/L
Inverse relationship is hard to visualize
80 kWnet, 100 kWhuse 360 V battery
Notes: Li: Lithium metal anode
Li2O2: lithium peroxide is the discharge product of the nonaqueous lithium oxygen electrochemical couple
Li/Li2O2 open: utilizes oxygen from the ambient atmosphere. Requires a compressor, removal of CO2 and H2O, and solvent management system
Li/Li2O2 closed: the cells are hermetically sealed within a pressure vessel that encloses a pure oxygen atmosphere.
LMRNMC: lithium and manganese rich nickel manganese cobalt oxide cathode material; this is an advanced Li-ion cathode in development worldwide and currently the subject of intense commercialization efforts by many companies.
Si: Composite silicon alloy anode; this advanced Li-ion anode material tends to be an alloy of multiple transition metals with silicon or a graphene/graphite based composite.
Gr: Graphite: the standard Li-ion anode intercalation material
NMC333: lithium nickel manganese cobalt oxide LiNi1/3Mn1/3Co1/3O2; a standard Li-ion cathode intercalation material
Tesla model S is a commercially available electric vehicle capable of 260 miles of electric range
Nissan Leaf is a commercially available electric vehicle capable of 70 miles of electric range
In the cost figure: non-materials refers to depreciation, labor costs, overhead, profit, and warranty costs; purchased items refers to cell tabs, state of charge controllers, packaging, etc; inactive materials refers to electrolyte, current collector foils, additives in the electrodes; pack integration refers to circuitry and electronics to allow for safe operation and integration into the vehicle

## Slide 18: Li/O2 Closed: volume and energy density breakdown
80 kWnet, 100 kWhuse 360 V battery
The dropping energy density
First loss is SOC window and efficiency
Second drop seems huge, but really small contribution to total volume
Inverse relation to volume is tricky
The systems level is the largest penalty (same in open-system)
What’s added moving left to right
Li/Li2O2: both anode and cathode
Electrodes: excess Li, carbon, binder, electrolyte
Bilayer: current collectors, ceramic
Cell: packaging, tabs
Module: packaging, SOC controllers
System: pressure vessel

## Slide 19: Systems level cost: Li/O2 similar to Li/LMRNMC
What’s in the bar graph?
Inactive materials: ceramic, current collectors, electrolyte, carbon, binder
Purchased items: tabs, packaging, state of charge controller
Non-materials: depreciation, labor, overhead, profit, and warranty
What’s in the uncertainty range?
Same designs in previous slide
Uncertainty in input costs
Catalyst cost is not in minimum cost estimate
80 kWnet, 100 kWhuse 360 V battery
Today’s costs $300-500/kWhuse
Notes: Li: Lithium metal anode
Li2O2: lithium peroxide is the discharge product of the nonaqueous lithium oxygen electrochemical couple
Li/Li2O2 open: utilizes oxygen from the ambient atmosphere. Requires a compressor, removal of CO2 and H2O, and solvent management system
Li/Li2O2 closed: the cells are hermetically sealed within a pressure vessel that encloses a pure oxygen atmosphere.
LMRNMC: lithium and manganese rich nickel manganese cobalt oxide cathode material; this is an advanced Li-ion cathode in development worldwide and currently the subject of intense commercialization efforts by many companies.
Si: Composite silicon alloy anode; this advanced Li-ion anode material tends to be an alloy of multiple transition metals with silicon or a graphene/graphite based composite.
Gr: Graphite: the standard Li-ion anode intercalation material
NMC333: lithium nickel manganese cobalt oxide LiNi1/3Mn1/3Co1/3O2; a standard Li-ion cathode intercalation material
Tesla model S is a commercially available electric vehicle capable of 260 miles of electric range
Nissan Leaf is a commercially available electric vehicle capable of 70 miles of electric range
In the cost figure: non-materials refers to depreciation, labor costs, overhead, profit, and warranty costs; purchased items refers to cell tabs, state of charge controllers, packaging, etc; inactive materials refers to electrolyte, current collector foils, additives in the electrodes; pack integration refers to circuitry and electronics to allow for safe operation and integration into the vehicle

## Slide 20: Summary of analysis to this point
Li/O2 closed architecture is more likely to meet automotive requirements than open approach, if developed.
For a large 100 kWhuse, 80 kWnet energy-storage system
  Cost (1st priority): Li/O2 is on par with Li/LMRNMC
  Volume (2nd): Li/LMRNMC is smaller than Li/O2
  Mass (3rd): Open system may be lighter, but closed system equivalent to Li/LMRNMC
Examine some sensitivities of the model
What role does risk play in R&D?

## Slide 21: Li/O2 Open: components volume sensitivity
Size of the gas utilization components is a key sensitivity
Scales with power and not energy
Advances needed for 55 L volume
  Zero vapor pressure electrolyte
  Reduced sensitivity to CO2/H2O
55 L components still leads to systems-level energy density less than Li/LMRNMC

## Slide 22: Li/O2 Closed: pressure vessel design variations
Al alloy has low mass & cost – used as baseline case in analysis
Carbon fiber attractive, fundamental challenges limit path forward
  Can’t flange (structural) or form tank around cells (temperature)
  Low thermal conductivity issue for heat transfer
Smaller inner diameter leads to higher mass, thus higher costs
cell
cell
80 kWnet, 100 kWhuse 360 V battery

## Slide 23: Comparative risk to achieving projected values:
Estimated values show mostly similar system-level values
  Si/LMRNMC being slightly costlier, moderately heavier
Value is best assessed in context of risk associated with achieving projected results
Qualitative risk factors compared to commercial Li-ion: High, Moderate, and Low
Cell Couple Anode/Cathode | Anode Chemistry Risk | Cathode Chemistry Risk | Cell Engineering Risk | System Engineering Risk
Li/O2 open | Morphology control Side reactions | Unknown electrolyte Insulating product | Li seal; Flow field; Li volume change | CO2/H2O removal Solvent capture
Li/O2 closed | Morphology control Side reactions | Unknown electrolyte Insulating product | Li seal Li volume change | Pressure vessel Thermal management
Li/LMRNMC | Morphology control Side reactions | Voltage fade Side reactions | Li volume change | Same as Li-ion
Si/LMRNMC | Side reactions | Voltage fade Side reactions | Si volume change | Same as Li-ion

## Slide 24: Comparative risk to achieving projected values:
Lithium metal is critical pathway to below $100/kWhuse
Si/LMRNMC presents moderate risk pathway to less than $125/kWhuse
Considering risks and potential rewards: Li/O2 should be considered only in a fundamental science context, not technology development for EVs
Qualitative risk factors compared to commercial Li-ion: High, Moderate, and Low
Cell Couple Anode/Cathode | Anode Chemistry Risk | Cathode Chemistry Risk | Cell Engineering Risk | System Engineering Risk
Li/O2 open | Morphology control Side reactions | Unknown electrolyte Insulating product | Li seal; Flow field; Li volume change | CO2/H2O removal Solvent capture
Li/O2 closed | Morphology control Side reactions | Unknown electrolyte Insulating product | Li seal Li volume change | Pressure vessel Thermal management
Li/LMRNMC | Morphology control Side reactions | Voltage fade Side reactions | Li volume change | Same as Li-ion
Si/LMRNMC | Side reactions | Voltage fade Side reactions | Si volume change | Same as Li-ion

## Slide 25: Acknowledgements
This work was supported as part of the Joint Center for Energy Storage Research, an Energy Innovation Hub funded by the U.S. Department of Energy, Office of Science, Basic Energy Sciences. This presentation has been created by UChicago Argonne, LLC, Operator of Argonne National Laboratory (“Argonne”). Argonne, a U.S. Department of Energy Office of Science laboratory, is operated under Contract No. DE-AC02-06CH11357.
Funding: DOE Office of Science, Joint Center for Energy Storage Research
Many colleagues within JCESR and throughout the larger GM organization provided guidance throughout this analysis

## Slide 26: 50 kWh Designs: Li/O2 open scales poorly with energy
Why your EV is more likely to be 50 kWh rather than 100 kWh (170mi vs 330mi):
Cars have a fixed volume (100-150 L)
Faster payback time on investment
80 kWnet, 50 kWhuse 360 V battery
Notes: Li: Lithium metal anode
Li2O2: lithium peroxide is the discharge product of the nonaqueous lithium oxygen electrochemical couple
Li/Li2O2 open: utilizes oxygen from the ambient atmosphere. Requires a compressor, removal of CO2 and H2O, and solvent management system
Li/Li2O2 closed: the cells are hermetically sealed within a pressure vessel that encloses a pure oxygen atmosphere.
LMRNMC: lithium and manganese rich nickel manganese cobalt oxide cathode material; this is an advanced Li-ion cathode in development worldwide and currently the subject of intense commercialization efforts by many companies.
Si: Composite silicon alloy anode; this advanced Li-ion anode material tends to be an alloy of multiple transition metals with silicon or a graphene/graphite based composite.
Gr: Graphite: the standard Li-ion anode intercalation material
NMC333: lithium nickel manganese cobalt oxide LiNi1/3Mn1/3Co1/3O2; a standard Li-ion cathode intercalation material
Tesla model S is a commercially available electric vehicle capable of 260 miles of electric range
Nissan Leaf is a commercially available electric vehicle capable of 70 miles of electric range
In the cost figure: non-materials refers to depreciation, labor costs, overhead, profit, and warranty costs; purchased items refers to cell tabs, state of charge controllers, packaging, etc; inactive materials refers to electrolyte, current collector foils, additives in the electrodes; pack integration refers to circuitry and electronics to allow for safe operation and integration into the vehicle

## Slide 27: Li/O2 Open: volume and mass breakdown

## Slide 28: Cell level: Simulated Li/O2 performance curves (I – V)
Target voltage at rated power
Electrode thickness designed from polarization curve
Notes: BatPaC is a freely available Li-ion Battery Performance and Cost model supported by DOE EERE-OVT and developed at Argonne National Laboratory. The model and supporting documentation are available from www.cse.anl.gov/batpac . BatPaC has been subjected to multiple public and private peer reviews that culminated in its use by the EPA in the 2017-2025 light duty vehicle GHG and CAFE rule.
This Li-O2 model uses BatPaC as a framework but substantially revises the performance calculation and adds new modeling capabilities to size and analyze the requirements of delivering, purifying, and/or enclosing a gaseous reactant.

## Slide 29: Systems level: The challenge of utilizing oxygen
Open system requires pretreatment of air
Li2O2 discharge product reacts with CO2 and H2O
  Removal of CO2 and H2O is necessary
  Target level uncertain, likely 1-10 ppm based on Li consumption
Pressure swing adsorption (PSA) provides continuous operation
  Temperature swing has unfavorable thermal lag time
  Expert sized 0.7 MPaa PSA for automotive applications
  Optimistically scaled for 0.3 MPaa (requires significant advances)
Volatile electrolyte requires solvent addition and capture
Closed system requires enclosure of pure oxygen
Cylindrical pressure vessel required
  How would one recharge tank?
  High pressure compressor unreasonable on or off-board

## Slide 30: Li/O2 Open: Engineering solutions enabling O2
Complicated system, but possible to meet purity requirements
Parasitic power and energy from compressing ambient air
Optimistic components for 80 kWnet
  89 L
  85 kg
  $1445
Component | Volume (L) | Mass (kg) | Cost ($)
Air filter | 4 | 2 | 15
Single-stage 0.3 MPa screw compressor, motor, cooling | 15 | 18 | 650
Two-stage 0.7 MPa screw compressor, motors, cooling | 30 | 36 | 1300
0.3 MPa pressure-swing adsorption system | 38 | 38 | 600
0.7 MPa pressure-swing adsorption system | 25 | 25 | 500
Solvent addition (100% vapor loss) | 14 | 12 | 70
Solvent capture (100% vapor loss) | 15 | 13 | 100
Fan for oxygen dilution to atmosphere | 3 | 2 | 10
Selected most optimistic, 0.3 MPaa based, architecture. 0.7 MPaa architecture is most feasible, but less attractive for system volume, mass, and cost

## Slide 31: Li/O2 Closed: Engineering solutions enabling O2
Enclose the cells within a pressure vessel (15-20 MPaa at 100% SOC)
Pure oxygen environment : better transport/discharge-kinetics?
Tank serves as battery enclosure – integrates into vehicle frame
Heat removal through conduction via Al heat sinks – limits tank diameter
First self-consistent Li/O2 design meeting automotive requirements.

## Slide 32: BatPaC Distribution
Over 600 unique users have downloaded the model
Fortune 500 companies, high-profile startups, academics
www.cse.anl.gov/batpac

## Slide 33: How BatPaC Matured
Late 2009, EPA expressed interest in using results of Argonne model in 2012-2016 rule making
This relationship became much closer when EPA asked Argonne and DOE to make the model the centerpiece of battery cost estimation in the 2017-2025 rule making
Using cost model in rule making required
  Update of model to improve both inputs and outputs
  Private peer reviews with OEMs (now more eager to help)
  Public peer review included representatives from: Tesla, GM, Dow Kokam, A123, and Prof. Whittingham
  Public release of model
Many updates and revisions were made before and after peer-review to produce the public versions: BatPaC v1.0 and v2.1